## Slide 1: Counters
Counting Clock Pulses in Lab 4

## Slide 2: The Temptation Don’t Do This!
Divide by 50,000,000
Four-Bit Counter
Divide by 50,000,000
Four-Bit Counter
50 MHz Clock
1Hz ‘Clock’
Output to Decoder and Hex Displays
4
This causes problems called ‘clock skew’ due to the fact that the 1 Hz ‘Clock’ really isn’t a clock signal – it’s derived from a counter in the first box.
This is OK

## Slide 3: The Solution
Divide by 50,000,000
Four-Bit Counter
Divide by 50,000,000
Four-Bit Counter
50 MHz Clock
1Hz Pulse
Output to Decoder and Hex Displays
4
ena
Add an Enable port to this counter
This counts from 0 to (50,000,000 – 1), then resets to 0 and repeats. It puts out a ‘1’ when the counter has a value of 0, otherwise it puts out a ‘0’. This is the 1Hz Pulse.