## Slide 1: Programmable Processors

## Slide 2: Programmable Processors
So far we’ve looked at ‘hard-wired’ or special purpose processors (like the SAD processor).
We’ll now look at programmable processors or ‘stored program’ processors.
Different tasks can be performed by changing the program.
Well-known examples: Pentium, PIC, ARM, Atmel AtMega, MIPS

## Slide 3: Datapath Side
Data Memory
n-bit
2-1 Mux
Register File
ALU
Datapath
n
n
n
n
n
Takes data from Data Memory
Stores it in Register File
Operates on it in ALU (puts it back into the Register File)
Can store Register File data back into Data Memory
Note the dual output Register File
We’ve built every piece of this already
addr
w_en
select
write, read
controls
function
select
n
From F. Vahid’s Digital Design

## Slide 4: Basic Datapath Operations
D[9] = D[0] + D[1] – requires a sequence of four datapath operations:
      0: RF[0] = D[0]
      1: RF[1] = D[1]
      2: RF[2] = RF[0] + RF[1]
      3: D[9] = RF[2]
Register file RF
Data memory D
ALU
n-bit
2x
1
Register file RF
Data memory D
ALU
n-bit
2x
1
Register file RF
Data memory D
ALU
n-bit
2x
1
LOAD operation
LOAD
LOAD
ADD
STORE
ALU operation
(like an ADD)
STORE operation
Each line here represents
one instruction; so it takes
four instructions to do this
add
From F. Vahid’s Digital Design

## Slide 5: Basic Architecture – Control Unit
D[9] = D[0] + D[1] – requires a sequence of four datapath operations:
      0: RF[0] = D[0]
      1: RF[1] = D[1]
      2: RF[2] = RF[0] + RF[1]
      3: D[9] = RF[2]
Each operation is an instruction
  Sequence of instructions = program
  Looks cumbersome, but that's the world of programmable processors – Decomposing desired computations into processor-supported operations
  Store program in Instruction memory
  Control unit reads each instruction and executes it on the datapath
    PC: Program counter – address of current instruction
    IR: Instruction register – current instruction
Register file RF
Data memory D
ALU
n-bit
2
x
1
Datapath
Instruction memory
Control unit
Controller
PC
IR
0: RF[0]=D[0]
1: RF[1]=D[1]
2: RF[2]=RF[0]+RF[1]
3: D[9]=RF[2]
a
From F. Vahid’s Digital Design
RF = Register File
D = Data Memory

## Slide 6: The Size of Things
Data memory (RAM): 256 X 16
Register file: 16 X 16 (dual output)
ALU: Two 16-bit inputs, 16-bit output
Instruction memory (ROM):32 X 16

## Slide 7: Basic Architecture – Control
Register file RF
Data memory D
ALU
n-bit
2
x
1
Datapath
Instruction memory
I
Control unit
Controller
PC
IR
0: RF[0]=D[0]
1: RF[1]=D[1]
2: RF[2]=RF[0]+RF[1]
3: D[9]=RF[2]
State Machine
From F. Vahid’s Digital Design

## Slide 8: Six-Instruction Processor
Instruction Set – List of allowable instructions and their representation in memory
Each of our instructions is 16 bits long
Most of them contain some address information
General form : operation source destination
NOOP instruction – 0000 0000 0000 0000
  STORE instruction – 0001 r3r2r1r0 d7d6d5d4d3d2d1d0
  LOAD instruction – 0010 d7d6d5d4d3d2d1d0 r3r2r1r0
  ADD instruction – 0011 ra3ra2ra1ra0 rb3rb2rb1rb0 rc3rc2rc1rc0
  SUBTRACT instruction – 0100 ra3ra2ra1ra0 rb3rb2rb1rb0 rc3rc2rc1rc0
  HALT instruction – 0101 0000 0000 0000
  ‘r’s are Register File locations (4 bits each)
  ‘d’s are Data Memory locations (8 bits each)

## Slide 9: NOOP Instruction
0000 0000 00000000
Always starts with 0000 (and contains nothing but zeros)
Actually is just 0000 xxxx xxxxxxxx, since the 12 bits following 0000 are ignored.
NoOp = No Operation
Just takes up space (or time)
Does not involve the Datapath
If your program starts executing a string of 0s, nothing (too) bad will happen.

## Slide 10: STORE Instruction
0001 r3r2r1r0 d7d6d5d4d3d2d1d0
Always starts with 0001
r3r2r1r0 is a 4-bit Register File address (source)
d7d6d5d4d3d2d1d0 is a Data Memory address (destination)
Moves 16 bits of data from the Register File to Data Memory
Example: 0001 1111 0010 1001b (or 0x1F29) means “move the data at Register File 0xF (15d) to Data Memory location 0x29 (41d)

## Slide 11: LOAD Instruction
0010 d7d6d5d4d3d2d1d0 r3r2r1r0
Always starts 0010
d7d6d5d4d3d2d1d0 is a Data Memory address (source)
r3r2r1r0 is a 4-bit Register File address (destination)
Moves 16 bits of data from Data Memory to the Register File
Example : 0010 00001010 0111b (or 0x20A7) means “move the data at Data Memory location 0x0A (10d) to Register File 7.”

## Slide 12: ADD Instruction
0011 ra3ra2ra1ra0 rb3rb2rb1rb0 rc3rc2rc1rc0
Always starts with 0011
ra3ra2ra1ra0 is a 4-bit Register File address (source for A)
rb3rb2rb1rb0 is a 4-bit Register File address (source for B)
rc3rc2rc1rc0 is a 4-bit Register File address (destination)
Adds the 16 bits of A to 16 bits of B, stores the result in C (all these in the Register File)
Example: 0011 0001 0010 0011b (or 0x3123) adds the data at Register File 1 to the data at Register File 2 and stores the result in Register File 3.

## Slide 13: SUBTRACT Instruction
0100 ra3ra2ra1ra0 rb3rb2rb1rb0 rc3rc2rc1rc0
Always starts with 0100
ra3ra2ra1ra0 is a 4-bit Register File address (source for A)
rb3rb2rb1rb0 is a 4-bit Register File address (source for B)
rc3rc2rc1rc0 is a 4-bit Register File address (destination)
Subtracts the 16 bits of B from the 16 bits of A, stores the result in C (all these in the Register File)
Example: 0100 0001 0010 0011b (or 0x4123) subtracts the data at Register File 2 from the data at Register File 1 and stores the result in Register File 3.

## Slide 14: HALT Instruction
0101 0000 00000000
Always starts 0101 and remainder is all 0s
Actually is 0100 xxxx xxxxxxxx, since all the bits following 0101 are ignored
Causes the processor to just stop (hard stop)
You need to reload it or reset it to get it going again.
Does not involve the Datapath

## Slide 15: First Program
Our program:
    0: RF[0] = D[0]
    1: RF[1] = D[1]
    2: RF[2] = RF[0] + RF[1]
    3: D[9] = RF[2]
    4: HALT
Becomes: LOAD 0 0 or 0010 00000000 0000b LOAD 1 1 or 0010 00000001 0001b ADD 0 1 2 or 0011 0000 0001 0010b STORE 2 9 or 0001 0010 00001001b HALT or 0101 0000 00000000b
This is what gets stored in Instruction Memory
0x2000
0x2011
0x3012
0x1209
0x5000

## Slide 16: The Register File (from HW6)
Register File
Clock
Reset
Write
Enable
Write
Addr
Write
Data
Read-A Enable
Read-A Addr
Read-B Enable
Read-B Addr
A Data
B Data
16
16
16
4
4
4

## Slide 17: The ALU (from HW6)
Datapath
Alu_s0 (function select)
16
16
16
A
B
s0
ALU
Q (Result)
module ALU( A, B, Sel, Q );
input [2:0] Sel; // function select
input [15:0] A, B; // input data
output [15:0] Q; // ALU output (result)
…
3
// This ALU has eight functions:
// if s == 0 the output is 0
// if s == 1 the output is A + B
// if s == 2 the output is A – B
// if s == 3 the output is A (pass-through)
// if s == 4 the output is A ^ B
// if s == 5 the output is A | B
// if s == 6 the output is A & B
// if s == 7 the output is A + 1;
// the additional functions are for future expansion

## Slide 18: Control-Unit and Datapath for Our Programmable Processor
PC
clr
up
5
IR
Id
16
16
I
data
addr
Controller
Control unit
Datapath
RF_W_wr
RF_Ra_addr
RF_Rb_addr
RF_Rb_rd
RF_Ra_rd
RF_W_addr
D_addr 8
D_wr
RF_s
Alu_s0
addr
D
wr
256
x
16
16
x
16
RF
16-bit
2
x
1
W_data
R_data
Ra_data
Rb_data
W_data
W_addr
W_wr
Ra_addr
Ra_rd
Rb_addr
Rb_rd
0
16
16
16
16
16
16
s
1
A
B
S
ALU
4
4
4
3
Detailed connections

## Slide 19: Controller State Machine
Control | Size
PC_clr | 1
PC_up | 1
IR_ld | 1
D_addr | 8
D_wr | 1
RF_s | 1
RF_W_addr | 4
RF_W_wr | 1
RF_Ra_addr | 4
RF_Ra_rd | 1
RF_Rb_addr | 4
RF_Rb_rd | 1
Alu_s0 | 3
Control Lines
Init
Fetch
Decode
NOOP
LOAD
STORE
ADD
HALT
PC_clr = 1
PC_up = 1
IR_ld = 1
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
D_addr = IR[7:0]
D_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 1
0011b
IR[15:12] == 0101b
0001b
0000b
0010b
SUB
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 2
0100b

## Slide 20: LOAD Anomaly
We need two LOAD states
because both the Data
Memory and the Register
File are both clocked
Init
Fetch
Decode
NOOP
LOAD_A
STORE
ADD
HALT
PC_clr = 1
PC_up = 1
IR_ld = 1
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
D_addr = IR[7:0]
D_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 1
LOAD_B
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0
SUB
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 2

## Slide 21: ATMEL 168 Microprocessor

## Slide 22: Altera’s ‘Soft’ Processor

## Slide 23: Processor Module Layout
Processor
Control
Unit
Datapath
Inst. Memory
PC
IR
State Machine
Control Unit
Data. Memory
Register File
ALU
Datapath
Top-Down
Design
Bottom-up
Implementation

## Slide 24: Top Level
Note: Contains Extra Debug Information

## Slide 25: Processor Level
Note: Contains Extra Debug Information

## Slide 26: Datapath Level
Note: Contains Extra Debug Information

## Slide 27: Controller Level
Note: Contains Extra Debug Information

## Slide 28: Procedure
Write a module (lowest level).
TEST IT!
Repeat until you have written all low-level modules.
Make sure your state machine is recognized as such by Quartus
Write the modules next level up (Control Unit, Datapath).
TEST THESE!
Write the Processor by instantiating Control Unit module and Datapath module and wiring them together.
At this point you should be able to test your entire processor in ModelSim. Remember you will need to create a ModelSim project not just a work library since you are using LPMs.
Final test for the Processor is running the program and inspecting Data Memory to make sure the correct value is stored in location 5.
NOTE: You can do your unit testing on the DE2 or you can use ModelSim – It’s probably better to test with ModelSim because you can more easily debug in this environment.