## Slide 1: Processor Extensions

## Slide 2: Simple Jump Instruction
Move the Program Counter by more than 1; even by a negative number
  Call it JUMP JUMP instruction – ???? bbbb bbbb 0000 where bbbb bbbb is an 8-bit signed number
So JUMP would add bbbb bbbb to the PC

## Slide 3: Control-Unit and Datapath for Our Programmable Processor
PC
clr
up
5
IR
Id
16
16
I
data
addr
Controller
Control unit
Datapath
RF_W_wr
RF_Ra_addr
RF_Rb_addr
RF_Rb_rd
RF_Ra_rd
RF_W_addr
D_addr 8
D_wr
RF_s
Alu_s0
addr
D
wr
256
x
16
16
x
16
RF
16-bit
2
x
1
W_data
R_data
Ra_data
Rb_data
W_data
W_addr
W_wr
Ra_addr
Ra_rd
Rb_addr
Rb_rd
0
16
16
16
16
16
16
s
1
A
B
S
ALU
4
4
4
3
Detailed connections
Becomes (signed) Adder

## Slide 4: JUMP State
Init
Fetch
Decode
NOOP
LOAD_A
STORE
ADD
HALT
PC_clr = 1
PC_up = 1
IR_ld = 1
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
D_addr = IR[7:0]
D_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 1
LOAD_B
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0
SUB
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 2
JUMP
PC_up = bbbb bbbb

## Slide 5: Jump If True (JNZ) Instruction
Move the Program Counter by more than 1 if some register evaluates to TRUE
  Call it JNZ (Jump if Not Zero - ???) JNZ instruction – ???? bbbb bbbb rrrr where bbbb bbbb is an 8-bit signed number and rrrr points to one of our Register File registers
So JNZ would add bbbb bbbb to the PC if rrrr is not zero
We are going to need some feedback from the ALU to the Controller

## Slide 6: Control-Unit and Datapath for Our Programmable Processor
PC
clr
up
5
IR
Id
16
16
I
data
addr
Controller
Control unit
Datapath
RF_W_wr
RF_Ra_addr
RF_Rb_addr
RF_Rb_rd
RF_Ra_rd
RF_W_addr
D_addr 8
D_wr
RF_s
Alu_s0
addr
D
wr
256
x
16
16
x
16
RF
16-bit
2
x
1
W_data
R_data
Ra_data
Rb_data
W_data
W_addr
W_wr
Ra_addr
Ra_rd
Rb_addr
Rb_rd
0
16
16
16
16
16
16
s
1
A
B
S
ALU
4
4
4
3
Detailed connections
Becomes Adder/Subtractor
Flags

## Slide 7: JUMP State
Init
Fetch
Decode
NOOP
LOAD_A
STORE
ADD
HALT
PC_clr = 1
PC_up = 1
IR_ld = 1
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
D_addr = IR[7:0]
D_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 1
LOAD_B
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0
SUB
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 2
JNZA
If (~Z)
PC_up = bbbb bbbb
JNZB
RF_Ra_addr=IR[3:0]
RF_ra_rd = 1
ALU_s0 = 3
Z is a ‘zero’ flag from ALU

## Slide 8: Adding Result Flags to ALU
A
B
S
Control
Lines
S is a function of A and B
Exactly what function
depends on the Control Lines
Result
Flags
(registered)

## Slide 9: Subtract Circuit from Text
We (you) can show V = carryout ^ xn-1 ^ yn-1 ^ sn-1
so you don’t need c3, which is buried in the Adder

## Slide 10: Signed Number Overflow
Figure 5.14. Examples of determination of overflow.
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
c
4
0 (carry to bit 4)
=
c
3
1 (carry to bit 3)
=
c
4
0
=
c
3
0
=
c
4
1
=
c
3
1
=
c
4
1
=
c
3
0
=
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
overflow = c3 ^ c4
in general, overflow = cn-1 ^ cn

## Slide 11: Signed Arithmetic Overflow Problem
Most of the time we’ll implement an adder with a ‘+’:
{Cout,Sum} = A + B + Cin;
So we just have ready access to the inputs and outputs of
the adder:
Cin
Adder
A
B
Sum
Cout

## Slide 12: Overflow Equations
claim: c3 = x3 ^ y3 ^ s3
Let’s see:
x3 ^ y3 ^ s3 = x3 ^ y3 ^ (x3 ^ y3 ^ c3)
= (x3 ^ y3) ^ (x3 ^ y3) ^ c3
= 0 ^ c3
= c3
In general,
cn-1 = xn-1 ^ yn-1 ^ sn-1
so
overflow = cn ^ cn-1 = cn ^ xn-1 ^ yn-1 ^ sn-1
= carryout ^ xn-1 ^ yn-1 ^ sn-1

## Slide 13: n-bit Adder with Carryout and Overflow
module addern( carryin, X, Y, S, carryout, overflow );
parameter n = 32;
input carryin;
input [n-1:0] X, Y;
output reg [n-1:0] S;
output reg carryout, overflow;
always @(X, Y, carryin) begin
{carryout, S} = X + Y + carryin;
overflow = carryout ^ X[n-1] ^ Y[n-1] ^ S[n-1];
end
endmodule

## Slide 14: Adding Flags to Our ALU
always @ ( A, B, S ) begin
Co = 0; // default
case ( S )
//…
2: {Co,Q} = A - B; // SUB
3: Q = A; // A
// …
endcase
// calculate the flags
V = Co ^ A[15] ^ B[15] ^ Q[15];
N = Q[15];
Z = ~|Q;
end // always
// register the flags
always @( posedge Clk ) begin
if ( En ) begin
F[0] = Z;
F[1] = N;
F[2] = V;
F[3] = Co;
F[15:4] = 0;
end // enabled
end // sequential loop

## Slide 15: Fun With Flags

## Slide 16: What Else Can We Do With These Flags?

## Slide 17: Jump if Less Than (JLT)
Init
Fetch
Decode
NOOP
LOAD_A
STORE
ADD
HALT
PC_clr = 1
PC_up = 1
IR_ld = 1
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
D_addr = IR[7:0]
D_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 1
LOAD_B
D_addr = IR[11:4]
RF_s = 1
RF_W_addr = IR[3:0
SUB
RF_W_addr = IR[3:0]
RF_W_wr = 1
RF_Ra_addr=IR[11:8]
RF_ra_rd = 1
RF_Rb_addr = IR[7:4]
RF_rb_rd = 1
ALU_s0 = 2
JLTA
If (N ^ V)
PC_up = bbbb bbbb
JLTB
?
N, V are flags from ALU

## Slide 18: We Can Now Do
if statements
for loops
While, repeat, etc.

## Slide 19: Subroutine Calls
Need a Stack (LIFO) to store PC so we can get back, registers
Stack Pointer (SP) points to next available slot in the stack
PUSH instruction – put something on the stack (like the PC)
POP instruction – take something off the stack
JSUB (jump to subroutine)
RET (return from subroutine)

## Slide 20: Interrupts
Once we have subroutine calls, it’s a short step to Interrupts
  A software interrupt (e.g., INT 3)
  An exception (like Overflow)
  Set up a timer that interrupts when it turns over or any other condition you wish
  A hardware interrupt (e.g, if GPIO[19] went from LOW to HIGH)
The addresses of Interrupt ‘subroutines’ (called Interrupt Handlers) are stored somewhere in Instruction Memory

## Slide 21: Definitely Not Least: An Assembler
Our program:
    0: RF[0] = D[0]
    1: RF[1] = D[1]
    2: RF[2] = RF[0] + RF[1]
    3: D[9] = RF[2]
    4: HALT
Becomes: LOAD 0 0 or 0010 00000000 0000b LOAD 1 1 or 0010 00000001 0001b ADD 0 1 2 or 0011 0000 0001 0010b STORE 2 9 or 0001 0010 00001001b HALT or 0101 0000 00000000b
This is what gets stored in Instruction Memory
0x2000
0x2011
0x3012
0x1209
0x5000