## Slide 1: TCES 330
Quartus Warnings Guide

## Slide 2: Quartus Warnings Guidelines
This guide applies to projects (homework, labs, exams) you are turning in.
Make sure you can account for all the warnings.
Right-click on the error or warning and select ‘Help’ from the context menu for more information (Firefox may be required).
Sometimes you are referred back to the Compilation Report – Go there and see what it says.
If you haven’t seen the warning before, it’s probably serious, so investigate.
It’s best to end up with a clean compile: no errors, no warnings.

## Slide 3: What to Avoid
All types of errors. The process (compile, simulation, etc.) won’t finish if you encounter an error.
The unused pins warning – even if we are not downloading to the board.
The output pin capacitance warning.
Hierarchy warnings (these are usually serious). They mean you haven’t wired in a module correctly.
Implicit Net Warnings are never good (usually you forgot to declare something).
Get rid of all Synopsys warnings (if there’s a clock in your circuit) by running the TimeQuest Timing Analyzer.
If you are building a state machine, make sure Quartus Netlist viewer shows a state machine!

## Slide 4: Sometimes Warnings
Unassigned pins – Don’t worry about this warning if you are not downloading to the DE2. The converse applies.
Pins stuck at Vcc or Ground – Make sure you know why this is occurring. Sometimes you expect this to happen.
Inferred latches are almost always bad.
The undefined clock warning if there’s a clock in your circuit.

## Slide 5: What Not To Worry About
The ‘Logic Lock’ warning
The ‘parallel compilation’ warning