## Slide 1: TCES 330
Verilog Style Guide

## Slide 2: Verilog Style Guidelines
This guide applies to all projects (homework, labs, exams) you are turning in.
Points will be assessed for failure to follow these guidelines
Initial comment block
In-code comments, as appropriate
Indentation
One module per file
Maximize use of modules (hierarchical design)
Maximize use of ‘parameter’s (maximize reusability).
Maximize use of ‘localparam’s (no magic numbers!)

## Slide 3: Initial Comment Block
// TCES 330, Spring 2010
// 3/27/2010
// R. Gutmann
// Lab 0
// This module represents a two-way switch with
// SW1 and SW2 representing the switch inputs and
// the signal f turns on (or off) the light.
module Light( SW, LEDG );
input [1:0] SW;
output [0:0] LEDG;
assign LEDG[0] = ( SW[0] & ~SW[1]) | (~SW[0] & SW[1] );
endmodule
Must contain:
Your name
The date
What assignment
Module summary

## Slide 4: In-code Comments
module Mux8( S, X, Y, M );
input S; // mux select line in
input [7:0] X, Y; // mux inputs
output [7:0] M; // mux output
// the mux:
assign M[0] = (~S & X[0]) | (S & Y[0]);
..
endmodule
Make some effort to explain your code; make it readable!

## Slide 5: Indentation
module Timer_1s( Clock, Out );
input Clock;
output reg Out;
reg [25:0]Q; // counter register
always @( posedge Clock ) begin
if ( Q == 26'h2FAF07F ) begin // check for max value
Q <= 26'b0; // reset counter
Out <= 1'b1; // output a 1
end
else begin
Q <= Q + 26'b1; // increment counter
Out <= 1'b0; // output a 0
end
end
endmodule